## Slide 1
Advanced Intelligent Textile Spinning Machine Monitoring, Fault Diagnosis and Condition-Based Maintenance System
An Arduino-Based Embedded Monitoring Prototype with Fault Prioritization
TEAM MEMBERS
Bharanidaran S - CB.SC.U4CSE25609 Dharshan S - CB.SC.U4CSE25614
Saswin S K - CB.SC.U4CSE25652 Harish Karthic U- CB.SC.U4CSE25659

## Slide 2
1 Why Monitor a Textile Spinning Machine?
Textile spinning machines operate continuously. Rotating spindle assemblies are continuously involved in operation. Continuous operation requires continuous condition monitoring.
Temperature
Abnormal temperature can indicate an operating problem
Vibration
Abnormal vibration can indicate a condition requiring inspection
Electrical
Electrical variations can indicate abnormal operation
Yarn
Yarn-break events can interrupt production
Package
Package-low events can interrupt production

## Slide 3
2 Problem Statement
“Abnormal machine conditions and production interruptions need to be identified, prioritized and recorded systematically to support timely inspection and reduce untracked downtime.”
EXISTING CHALLENGES
1 Detection
Identify abnormal machine conditions.
2 Prioritization
Determine which fault requires attention first.
3 Tracking
Maintain recent readings and event information.
Faults may require manual observation.
Multiple notifications may not be equally urgent.
Event history can be difficult to track consistently.

## Slide 4
3 Proposed Solution
Machine Conditions
Sensor / Event Inputs
Arduino Mega 2560
Rule-Based Detection
Circular Buffer + Priority Queue
Machine State & Alerts
THE PROTOTYPE
An educational prototype — not a complete industrial control system.
•
Monitors selected machine conditions.
•
Detects configured abnormal conditions.
•
Prioritizes selected fault notifications.
•
Displays operating state and alerts.
•
Maintains recent readings and supported event records.

## Slide 5
4 Project Objectives & Scope
OBJECTIVES
•
Monitor selected temperature, acceleration and electrical readings.
•
Detect configured abnormal conditions.
•
Prioritize selected fault notifications.
•
Display operating state and alerts.
•
Maintain recent readings and supported event records.
IN SCOPE
OUT OF SCOPE
•
Arduino-based prototype
•
Wokwi environment
•
Five software-modeled spindle stations
•
Rule-based detection
•
Local displays and alerts
•
Circular Buffer
•
Priority Queue
•
Validated machine-learning prediction
•
Independent physical sensing for all five stations
•
Guaranteed automatic industrial protection
•
Certified industrial deployment

## Slide 6
5 System Architecture
INPUTS
CONTROLLER
Arduino Mega 2560
SOFTWARE PROCESSING
OUTPUTS
•
DS18B20 Temperature Sensor
•
MPU6050 Accelerometer
•
INA219 Voltage/Current Monitor
•
Rotary Encoder
•
Yarn-Break Button
•
Package-Low Button
•
Alarm Acknowledge Button
•
Input acquisition
•
Data updates
•
Threshold checks
•
Circular Buffer
•
Rule-based detection
•
Priority Queue
•
Machine-state tracking
•
Statistics updates
•
SSD1306 OLED
•
Serial Monitor
•
Green LED
•
Yellow LED
•
Red LED
•
Buzzer
•
Optional microSD

## Slide 7
Component | Function | Project Use
Arduino Mega 2560 | Main controller | Coordinates acquisition, logic and outputs
MPU6050 | Accelerometer | Provides acceleration data as vibration indicator
INA219 | Power monitor | Measures voltage and current
DS18B20 | Temperature sensor | Measures operational temperature
Rotary Encoder | Input device | Adjusts target value and navigation
SSD1306 OLED | Display | Machine-status interface
LEDs & Buzzer | Indicators | Visual and audible alerts
Push Buttons | Simulated inputs | Yarn-break, package-low, alarm acknowledgement
6 Hardware Components

## Slide 8
7 How the System Works
After the history update, the cycle returns to Start Monitoring Cycle.
Abnormal Condition?
Start Monitoring Cycle
Acquire Sensor Readings
Update Circular Buffer
Evaluate Rules
NO
Continue Monitoring
YES
Create Fault Event
Insert into Priority Queue
Process Highest Priority
Update Machine State & Alarms
Refresh OLED / Serial Monitor
Update History

## Slide 9
8 Fault Detection & Machine States
Alarm acknowledgement indicates that the operator has seen the alert; it does not automatically resolve the underlying fault.
NORMAL
Readings within configured limits
Output: Green LED
WARNING
Examples:
Output: Yellow LED
CRITICAL
Examples:
Output: Red LED + Buzzer
•
Abnormal temperature
•
Electrical out-of-range
•
Package-low event
•
Abnormal vibration
•
Yarn-break event
•
Configured critical condition

## Slide 10
9 Circular Buffer
Recent sensor readings need to be maintained efficiently. New sensor sample arrives. Store at current write position. Advance write position. Wrap around at the end. Overwrite the oldest sample when full.
Fixed memory usage
No array shifting
Rolling / recent calculations
Insertion: O(1)
BEFORE (FULL)
new value 36 arrives — write pointer at slot 0 (oldest = 31)
AFTER
write pointer advances to slot 1; after slot 4 it wraps to slot 0
31
32
33
34
35
36
32
33
34
35

## Slide 11
10 Priority Queue Using Max Heap
These are example software priorities, not measured risk values.
Example max-heap: the highest-priority event sits at the root. The system does not necessarily process events in the order they arrive. Instead, it selects the event with the highest assigned priority.
COMPLEXITY: INSERT
O(log n)
COMPLEXITY: REMOVE HIGHEST PRIORITY
O(log n)
COMPLEXITY: VIEW HIGHEST PRIORITY
O(1)
Critical Vibration Priority 3
Over-Temperature Warning Priority 2
Package-Low Event Priority 1

## Slide 12
11 Circuit Design & Simulation
Arduino Mega 2560 · MPU6050 · INA219 · DS18B20 · OLED · Rotary encoder · Push buttons · LEDs · Buzzer
[Insert Wokwi circuit screenshot here]
COMMUNICATION INTERFACES
I²COLED, MPU6050, INA219
OneWireDS18B20
Digital inputsEncoder and buttons
Digital outputsLEDs and buzzer
SPIOptional microSD

## Slide 13
12 Simulation Working & Example Scenarios
Yarn-break → Critical alert Package-low → Warning alert
[Wokwi screenshot]
[Wokwi screenshot]
[Wokwi screenshot]
Scenario 1 — NORMAL
Scenario 2 — WARNING
Scenario 3 — CRITICAL
Input within limits
→ Normal state
→ Green LED
Threshold crossed
→ Warning event
→ Yellow LED
Critical condition / simulated fault
→ High-priority event
→ Red LED + Buzzer

## Slide 14
13 Testing, Limitations & Future Improvements
TEST CASES
CURRENT LIMITATIONS
FUTURE IMPROVEMENTS
•
Normal input
•
Temperature threshold
•
Vibration threshold
•
Yarn-break
•
Package-low
•
Multiple events
•
Buffer wraparound
•
Queue selection
•
Alarm acknowledgement
•
microSD logging
•
Five spindle stations are software-simulated
•
Rotary encoder is a setpoint control, not an RPM sensor
•
Vibration analysis is simplified
•
Electrical measurements require calibration
•
Thresholds are rule-based
•
microSD requires simulator compatibility testing
•
Actual RPM measurement sensor
•
Independent physical sensors for individual spindle stations
•
Real-machine measurements
•
Calibrated thresholds

## Slide 15
14 Conclusion
INPUTS
ARDUINO
DETECTION
BUFFER + QUEUE
FAULT PRIORITIZATION
ALERTS
The prototype demonstrates embedded monitoring of selected machine conditions.
Rule-based logic identifies configured warnings and simulated fault events.
Circular Buffer stores recent readings efficiently.
Binary Heap Priority Queue prioritizes pending notifications.
Embedded systems and data structures can work together for condition monitoring.
“The system is an educational monitoring prototype. Real-machine deployment would require additional sensing, calibration, validation and appropriate industrial safety engineering.”
THANK YOU